## Slide 1: Airspace Management
Lesson 2
Civil Aviation University of China
Civil Aviation University of China

## Slide 2: Learning Objectives
Objective:
  State the objective of ASM
  State the functions of ASM
  Define the three types of Special Use Airspace
  List the names of the part of airspace for the use of commercial flights
  State the purpose of airspace classification
References:
  EUROCONTROL HANDBOOK FOR AIRSPACE MANAGEMENT
  EUROCONTROL AIRSPACE STRATEGY FOR THE ECAC STATES

## Slide 3: Airspace Users and Activities
Airlines – commercial transportation
Military – Training, Exercises, Operations
Police, Customs – Crime Prevention
GA – All other, including Leisure, Sports…
All these activities should be accommodated
Commercial Air Traffic in China

## Slide 4: Objectives of ASM
The objective of ASM is to maximize, within a given airspace structure, the utilization of available airspace by dynamic time-sharing and, at times, segregation of airspace among various categories of users based on short-term needs.
Close co-operation between the appropriate authorities on expected and actual utilization of the temporary reserved airspace should result in information being readily available to all parties concerned, i.e. commercial air transport, military operational air traffic and general aviation.

## Slide 5: Functions of ASM
collection and evaluation of all requests which require temporary airspace allocation;
planning and allocation of the required airspace to the users concerned where segregation is necessary;
activation or de-activation of such airspace within adequately narrow time tolerances, in close co-operation with ATC units and civil or military units concerned.
dissemination of detailed information, both in advance and in real time, to all parties concerned.

## Slide 6: World Air Traffic Routes

## Slide 7
Flight Information Regions (FIR)
Notes: Flight information region (FIR). An airspace of defined dimensions within which flight information service and alerting
service are provided.

## Slide 8: Airspace reservations and restrictions
Reservations
Special Use Airspace
  Prohibited Area
  Restricted Area
  Danger Area

## Slide 9: Airspace for Commercial Flights
Airways and Air-routes (AWY)
Terminal Control Areas (TMA)
Aerodrome Control Zones (CTZ)
AWY
TMA
TMA
CTZ
CTZ
AWY
Uncontrolled Airspace

## Slide 10: Controlled Airspace
Control Areas
Control Sectors

## Slide 11: Airspace Design
Design of Airspace Structures
Design of Restricted Airspace and Reserved Airspace
Design of Airways and Sectors
Design of Terminal Airspace

## Slide 12: Airspace Design Examples
Establish Specialized Routes

## Slide 13: Airspace Design Examples
Established Specialized Sectors

## Slide 14: Airspace Design Examples
Organize ATS Routes

## Slide 15: Airspace Design Examples

## Slide 16: Airspace Design Examples
San Francisco Bay Area – West Flow

## Slide 17: Airspace Design Examples
San Francisco Bay Area – East Flow

## Slide 18: Airspace Design Examples
Departure from Runway 36L Beijing Capital

## Slide 19: Airspace Design Examples
Arrivals to Land North at Beijing Capital

## Slide 20: Air Traffic Control Units
Airways and Air-routes ----- Area/Airway Control Centre
Terminal Control Areas ----- Terminal/Approach Control
Aerodrome Control Zone ----- Tower control

## Slide 21: Classification of Airspace
The purpose of airspace classification
  Different degree of control for different activities
  Different rules for different activities
  Different service for different activities
  Different equipage requirements for different activities

## Slide 22: Classification of Airspace
UK Airspace Classification
Class G
Class B UIR
Class F Advisory Route
Airways
Class A
CTA
TMA
Class A
Control Zone
ATZ
MATZ
Class G
Class D
CTR
Class E
Class G
FL660
FL245

## Slide 23: Classification of Airspace
UK Airspace Classification

## Slide 24: Classification of Airspace
US Airspace Classification

## Slide 25: Classification of Airspace
US Airspace Classification
US Airspace Classification

## Slide 26: China Airspace Classification
Classification of Chinese airspace
  A – High level airspace
  B – Medium and low level airspace
  C –Terminal (Approach) control area
  D – tower control zone
  Unclassified in fact!
All airspace is controlled due to historical reasons

## Slide 27: Simplified Airspace Organization
N
K
U
Intended
Traffic
Environment
FL X
FL Z
Known
Traffic
Environment
Unknown
Traffic
Environment
K
N

## Slide 28: Future Airspace Structure

## Slide 29: Questions
What are the functions of ASM?
What are three types of SUA?
Why is airspace classified?
What are the blocks of airspace for commercial flights?
What ATC units are responsible for these blocks of airspace?
Should Chinese airspace be “reclassified”?