## Slide 1: Telecommunication & Observation SYSTEM
Case Study: Requirements definition

## Slide 2: Stakeholders requirements definition
Part 1

## Slide 3: Activities
Define functional
boundaries
Verify consistency,
exhaustiveness and establish traceability
Define
operational
scenarios
Define expected
measures of
effectiveness
(performances)
Identify
situations of life
and stakeholders
Quantify
and classify
the needs
Define
operational conditions
Define
purpose and mission
Define operational concepts or technological concepts
Express each
stakeholder
requirement individually
Define physical
boundaries
Identify
Delimit
Understand Dynamics
Develop Requirements

## Slide 4: Case study
Identify the purpose of the system
  Why does the system exist ? What for ?
Identify the mission of the system
  What does it do ?
Define the objectives of the system
  What level of performance/efficiency ?
Identify
situations of life
and stakeholders
Define
purpose and mission
Identify

## Slide 5: Example of purpose and missions
system purpose mission objectives
A car manufacturer
One
production line
?
?
?
?
?
?
why ?
what ?
how much ?

## Slide 6: Example of purpose and missions
system purpose mission objectives
A car manufacturer
One
production line
?
?
?
?
?
?
why ?
what ?
how much ?
make money,
provide jobs,
provide means for transportation
identify, design,
produce, sell cars
2 new models per year
10 5 cars per year
produce cars
assemble parts
25 000 cars

## Slide 7: Case study
Identify the purpose of the TOS
  Why does the system exist ? What for ?
Identify the mission of the TOS
  What does it do ?
Define the objectives of the TOS
  What level of performance/efficiency ?
Identify
situations of life
and stakeholders
Define
purpose and mission
Identify

## Slide 8: Case study
Identify the stakeholders
  Focus on the Operation phase
  Identify external actors
    Persons or organisations (operators who will operate or maintain the system, users who will exploit it)
    Other systems interacting with or constraining the System of Interest
Identify
situations of life
and stakeholders
Define
purpose and mission
Identify

## Slide 9: Case Study
Identify the service functions
  Functions of the systems with respect to external actors
  Apply the Octopus method
  You can model the result with a use case diagram
Define functional
boundaries
Define operational concepts or technological concepts
Define physical
boundaries
Delimit

## Slide 10: Functional context
System of Interest
Operator
User
Service function
Service function
Environment
Other
system
Service function
Maintenance
Service function: Expected system function, considering the system as a black-box (no information on the function implementation).
Service function
Constraints

## Slide 11: Case Study
Identify the Physical interfaces
Define functional
boundaries
Define operational concepts or technological concepts
Define physical
boundaries
Delimit

## Slide 12: Physical context
System of Interest
Operator
User
Environment
Other
system
Maintenance
The physical interface is the link which will support the corresponding service function. It can be:
A physical connector
A contact between physical surfaces
A communication protocol
An input or communication device
…
Constraints
Physical interface
Physical interface
Physical interface
Physical interface

## Slide 13: Case Study
Identify the operational concepts
"Operational concepts" are general way or approach or strategy of operation / utilization: basic options of how will be used the system in operation / in service.
  Example: a completely automated system, or a system which let human to decide on operation tasks and to make decisions.
Define functional
boundaries
Define operational
concepts
or technological
concepts
Define physical
boundaries
Delimit

## Slide 14: Case Study
Identify the technological concepts
"Technological concepts" are technological options for the global usage of the system.
Example: a solution which is based on "electronic" or "pneumatic" technology
Define functional
boundaries
Define operational
concepts
or technological
concepts
Define physical
boundaries
Delimit

## Slide 15: Case Study
Describe the following operational scenarios
  1) From initial storage to the detection and observation of a fire
  2) Detection and correction of a system failure
  … with sequence diagrams
Define
operational
scenarios
Define expected
measures of
effectiveness
(performances)
Define
operational conditions
Understand Dynamics

## Slide 16: Case Study
Identify the main operational conditions
  From the initial needs
  … and more if needed
Define
operational
scenarios
Define expected
measures of
effectiveness
(performances)
Define
operational conditions
Understand Dynamics
Notes: The operational conditions express conditions of execution (example : availability, safety, security, human factors, environmental conditions).
Operational constraints are added, for instance physical dimensions or imposed solutions.

## Slide 17: Case Study
Identify performances
  From the initial needs
  … and more if needed
Define
operational
scenarios
Define expected
measures of
effectiveness
(performances)
Define
operational conditions
Understand Dynamics

## Slide 18: Usefulness of classification
Operational requirement | Identify the situations of life to be taken into account and the corresponding operational conditions
Functional Requirement | Know the various transformations to be operated on energy, material and information
Measure of effectiveness | Define the field of application of these transformations
Constraint | Identify the limits applicable to physical architectures and to components
Interface | Participate to exchanges between various sets
Validation | Take into account the various elements of validation which have an impact on architectures
Sorting requirements into categories allow to simplify their interpretation

## Slide 19: Case Study
  Define the Stakeholder Requirements
    expected services
    expected performances
    expected interfaces
    operational conditions
    Constraints
    Validation
  .. from the initial needs, and the previous analysis and diagrams
Verify consistency,
exhaustiveness and establish traceability
Quantify
and classify
the needs
Express each
stakeholder
requirement individually
Develop Requirements

## Slide 20: Exercise
Telecommunication and Observation System
Write down some Service requirements of the TOS
Guidelines
  Use case and operational scenarios are
  good sources for service requirements
Time: 15 min

## Slide 21: Exercise
Telecommunication and Observation System
Write down some Performance requirements of the TOS
Guidelines
  Typical sources:
    Needs with quantitative or qualitative
    Information
Time: 10 min

## Slide 22: Exercise
Telecommunication and Observation System
Write down Operational conditions requirements of the TOS
Guidelines
  Typical source: any need related to « when »,
  « where », « under which conditions »
Time: 10 min

## Slide 23: Exercise
Telecommunication and Observation System
Write down Interface requirements of the TOS
Guidelines
  Typical sources are the context diagrams
Time: 10 min

## Slide 24: Exercise
Telecommunication and Observation System
Write down Constraints requirements of the TOS
Guidelines
  Typical sources is regulations
Time: 5 min

## Slide 25: Exercise
Telecommunication and Observation System
Write down Validation requirements of the TOS
Time: 5 min

## Slide 26: Stakeholder Requirements Definition Process
Requirements
Analysis
Technical
Requirements
Document
Stakeholders
Requirements
document
  The purpose is to transform the stakeholder, requirement-driven view of desired services into a technical view of a required product that could deliver those services

## Slide 27: Activities of the System Requirements Definition Process
Define
functional
requirements
Verify consistency,
exhaustiveness and establish traceability
Define
Lifecycle
constraints
Define physical
constraints
Analyse boundaries
and interactions
with the context
Analyse operational scenarios and modes
Define interface requirements
Express each
technical
requirement individually
Define performance
requirements
Analyse
Define
Constrain
Develop Requirements
Define
operational Requirements
Notes: Note: Write preferably measure of effectiveness requirements (performance requirements) separately from functional requirements, because during design, it is possible that such a requirement is allocated to several functions.

## Slide 28: Case Study
  Identify the technical functions supporting the service functions of the system
Define
functional
requirements
Define interface requirements
Define performance
requirements
Define
Define
operational Requirements

## Slide 29: Case Study
  Analyse two Stakeholder Requirements of each category and refine them into technical requirements
    expected services
    expected performances
    expected interfaces
    operational conditions
    Constraints
    Validation
Define
functional
requirements
Define interface requirements
Define performance
requirements
Define
Define
operational Requirements

## Slide 30: Detailed analysis
Analyse boundaries
and interactions
with the context
Analyse operational scenarios and modes
Analyse
Identify a first level physical(organic) architecture of the system
  Identify internal sub_systems
  Define their interface and interactions
  SysML tool: Internal Block Diagram
  It can be useful to extend the existing operational scenarios (Sequence Diagrams) with the new elements

## Slide 31: Verification&Validation
Part 3

## Slide 32: Verify these requirements
  The display shall be bright blue or yellow
  The system is able to operate in daylight conditions
  The hull of the satellite shall be water-proof
  The fuselage shall be 100% resistant to impacts
  The speed of the cooling fan shall be 10000 rpm (TBC)
  The termination resistors shall not be located on the main board
  The FCSC shall have a MTBF of more than six months
  The main calculator shall be composed of two computers with an Ethernet connection

## Slide 33: Case Study
  For each technical requirement:
    Verify that it is of good quality
    Identify one verification mean
    Identify one verification objective
    Link the requirement to the corresponding stakeholder requirements
Verify consistency,
exhaustiveness and establish traceability
Express each
technical
requirement individually
Develop Requirements